## Slide 1: Dependable and Safety-critical software for space applications
Kristoffer Nyborg Gregertsen, PhD
NTNU, 2018-10-26
© ESA/Hubble

## Slide 2: Content
Real-time systems group at SINTEF Digital
Dependability and safety for space and avionics
  Standards and methodologies
  Ada 2012, SPARK 2014 and the Ravenscar profile
  MISRA C/C++ and Frama-C
Break?
I3DS project, a modular sensor suite for space robotics

## Slide 3: SINTEF is one of Europe’s largest independent research organisations
75
Nationalities
4000
Customers
2000
Employees
NOK 3.1 billion
Revenues
NOK 450 MILL
International sales
Notes: Detailed facts & figures and more info
During 2016, SINTEF worked on 5,722 projects for 3,952 small and large customers. Forty-one per cent of gross operating revenues (NOK 3.147) billion were generated directly from contract research projects for Norwegian private sector customers.
International sales amounted to NOK 448 million. Fourteen per cent of SINTEF's operating revenues were generated from international projects. In 2016, SINTEF had customers in 63 countries worldwide, and EU-funded projects constituted about 50 per cent of international sales.
At the turn of the year SINTEF had 1,960 employees. Fifty-six per cent of our researchers have doctorate degrees, compared with 44 per cent in 2009. The proportion of women among our research scientists is 29 per cent, and 33 per cent among managerial personnel.
Twenty-two per cent (432) of SINTEF's employees come from as many as 74 countries outside Norway. SINTEF's overseas employees provide a valuable source of scientific and cultural expertise. The majority of employees from outside Norway are from Germany and France.

## Slide 4: About me
SINTEF Digital – Department of Mathematics and Cybernetics
Research manager for automation and real-time systems
PhD in cybernetics from NTNU on real-time system support in Ada with execution time for interrupts
Part of PhD work in ISO-standard

## Slide 5: Research group
8 researchers
Development, integration, testing
Safety assessment and validation
Industrial automation
Real-time systems
We are hiring research scientist!
(+3)

## Slide 6: Real-time systems
Correctness of result depends on time
  Systems that interact with physical environment
  Explicit deadlines – predictable execution
Different classes of criticality:
  Soft real-time systems – some deadline misses tolerable
  Firm real-time systems – result has no value after deadline
  Hard real-time systems – system failure to miss deadline

## Slide 7: Dependability and safety
Real-time systems usually also safety-critical:
  Control physical processes, potentially harmful!
  Fault → Error → Failure
  Formal verification
  Error handling
  Multiple version redundancy…
Industrial systems need high availability
Robotics systems may need high reliability

## Slide 8: Standards for space applications
European Cooperation for Space Standardization (ECSS)
  Standards used by ESA and European national space agencies
  Open access to standards at http://ecss.nl (needs user registration)
Some central documents for safety-critical software
  ECSS-S-ST-00-01C – Glossary of terms
  ECSS-Q-ST-30C Rev.1 – Dependability
  ECSS-Q-ST-80C Rev.1 – Software product assurance
  ECSS-E-ST-40C – Software general requirements
The documents are coherent, reasonable and quite easy to read!

## Slide 9: ECSS-S-ST-00-01C definitions
Dependability: The extent to which the fulfilment of a required function can be justifiably trusted. Its main components are reliability, availability and maintainability. Dependability shall be considered in conjunction with safety.
Availability: Ability of an item to be in a state to perform a required function under given conditions at a given instant of time or over a given time interval, assuming that the required external resources are provided.

## Slide 10: ECSS-S-ST-00-01C definitions
Reliability: The ability of an item to perform a required function under given conditions for a given time interval. Generally, reliability performance is quantified using appropriate measures. In some applications these measures include an expression of reliability performance as a probability, which is also called reliability.
Maintainability: Ease of performing maintenance on a product. Maintainability can be expressed as the probability that a maintenance action on a product can be carried out within a defined time interval, using stated procedures and resources.

## Slide 11: Dependability relationships
Functional
Failure
Error intensity
Maintenance intensity
Possion intensities → Markov chain
Maintenance not possible → Only reliability
Availability: Faction of time in functional state
Reliability: Time from functional to first failure

## Slide 12: ECSS-S-ST-00-01C definitions
Safety: State where an acceptable level of risk is not exceeded. Here risk relates to fatality, injury or occupational illness; damage to launcher hardware or launch site facilities; damage to an element of an interfacing manned flight system; the main functions of a flight system itself; pollution of the environment, atmosphere or outer space; and damage to public or private property.
Safety critical function: Function that, if lost or degraded, or as a result of incorrect or inadvertent operation, can result in catastrophic or critical consequences.

## Slide 13: ECSS-S-ST-00-01C definitions
Certification: Procedure by which a party gives formal assurance that a person or an organization acts, or a product is, in compliance with specified requirements.
Assurance: Planned and systematic activities implemented, and demonstrated as needed, to provide adequate confidence that an entity fulfils its requirements.

## Slide 14: ECSS-Q-ST-30C definition of severity
Severity | Level | Dependability consequences
Catastrophic | 1 | Failure propagation (for lower-level systems analysis)
Critical | 2 | Loss of mission
Major | 3 | Major mission degradation
Minor or Negligible | 4 | Minor mission degradation or any other effect

## Slide 15: ECSS-Q-ST-30C definition of severity
Severity | Level | Safety consequences
Catastrophic | 1 | Loss of life, life-threatening or permanently disabling injury or occupational illness. Loss of system. Loss of an interfacing manned flight system. Loss of launch site facilities. Severe detrimental environmental effects.
Critical | 2 | Temporarily disabling but not life-threatening injury, or temporary occupational illness. Major damage to an interfacing flight system Major damage to ground facilities Major damage to public or private property Major detrimental environmental effects
Major | 3 | ---
Minor or Negligible | 4 | ---

## Slide 16: ECSS-Q-ST-30C definition of criticality
Severity | Function criticality | Criteria to assign criticality categories to functions
Catastrophic (Level 1) | I | A function that if not or incorrectly performed, or whose anomalous behaviour can cause one or more feared events resulting in catastrophic consequences.
Critical (Level 2) | II | A function that if not or incorrectly performed, or whose anomalous behaviour can cause one or more feared events resulting in critical consequences.
Major (Level 3) | III | A function that if not or incorrectly performed , or whose anomalous behaviour can cause one or more feared events resulting in major consequences.
Minor or Negligible (Level 4) | IV | A function that if not or incorrectly performed , or whose anomalous behaviour can cause one or more feared events resulting in minor or negligible consequences.

## Slide 17: Discuss!
Does safety considerations apply for CubeSats?
What about dependability?

## Slide 18: ECSS-Q-ST-80C software assurance
Goal: Provide adequate confidence to the customer and to the supplier that the developed or procured/reused software satisfies its requirements throughout the system lifetime.
Defines requirements for software product assurance to meet this:
  Organization and responsibility
  Procurement
  Tools, methodologies, metrics
  Training
Specifies the required plans and reports for different project stages

## Slide 19: ECSS-Q-ST-80C software categories
The standard defines four software criticality categories:
  A: Software involved in category I functions, AND no compensating provisions exist. OR the software is included in compensating provisions for category I functions.
  B: Software involved in category I functions AND at least one of the following compensating provisions is available: a hardware implementation, a software implementation of category A, or an operational procedure. OR the software is involved in category II functions AND no compensating provisions exist. OR the software is included in compensating provisions for category II functions.
  C: Same as above but for category II and III.
  D: Same as above but for category III and IV.

## Slide 20: ECSS-E-ST-40C general requirements
General software requirements for different stages of project:
  Development, verification and validation
  Operation and maintenance
Specifies requirements for different software categories such as
  Code test coverage (100% for A/B, only by agreement for C/D)
  Schedulability analysis
  Formal proof
Specifies the required plans and reports for different project stages

## Slide 22: Civil aviation software standards
DO-178C: Software Considerations in Airborne Systems and Equipment Certification. Defines Software Level or Design Assurance Level (DAL), documentation in certification artifacts, Low- and High-Level Requirements, traceability analysis…
Supplements to standard:
  DO-330: Software Tool Qualification Considerations
  DO-331: Model-Based Development and Verification
  DO-332: Object-Oriented Technology and Related Techniques
  DO-333: Formal Methods
No fatalities in civil aviation world-wide in 2017!!!

## Slide 23: Summary of software standards
Product, functionalities, life-time, dependability and safety
Specify the criticalities, severities, and assurance levels
Specify how the software assurance process is done
Specify how the software development process is performed
Plans, audits, certification, training, maintenance…
LOTS of documentation involved!

## Slide 24: Discuss!
What software assurance level is sufficient for the NTNU cubesat projects?
If sold to ESA?

## Slide 25: Programming languages and tools
Programming languages and tools for safety-critical systems
  Ada 2012 programming language and SPARK 2014
  C programming language, MISRA C/C++ and Frama-C
  Rust programming language, new kid on the block, not further mentioned
Compilers, verification tools, run-times, RTOS, certification
Should avoid prejudice and "holy language wars"
What is the best tool for the job?

## Slide 26: Ada programming language
Ada is a general-purpose programming language that has been specifically designed for safe and secure programming.
Originates from late 70s where US DoD ordered a programming language to replace hundreds of languages used for its projects.
First ISO-standard was Ada 83, current standard is Ada 2012.
While it is general purpose, Ada is today most used in safety-critical domains such as avionics, space, train control and similar.
Ada Lovelace

## Slide 27: Some features in Ada 2012
Strong typing
Rich type system
  Integer and floating-point ranges
  Array and record types
  Access types
Object-orientation
Large system with packages
Tasking support in language
  Tasks, priorities and scheduling
  Task rendezvous and protected objects
  Interrupt handling
High-precision clocks
Exception handling
Programming by contract

## Slide 28: SPARK 2014
Sub-set of Ada 2012 for formal analysis:
  No access types (although work in progress for limited support)
  No side effects for functions and expressions
  No exceptions and limited tasking
Uses the new Ada 2012 aspect feature:
  Flow-control for variables, including (encapsulated) global variables
  Contracts for functions and procedures
Basic usage proves program flow and absence of run-time errors
Full usage gives formal proof of program properties

## Slide 29: Flow-control
Analyse flow of variables
  Specify input and output of subprograms and how they relate
  Uninitialized data and unused data
Includes analysis of global variables
  Common cause of errors in large systems
  Also global variables that are private in packages
Volatile variables with effective reads and writes
  For instance used for device drivers
Abstract state for packages, refined in private implementation
"Silver level"

## Slide 30: Contracts and formal proof
Use pre/post-condition aspects in Ada 2012
  What must be true when the subprogram is called
  What must be true after the subprogram has been called
  Helper pragmas to assist the formal proof
Also for object-orientated class threes
  Pre-conditions must be same or weaker than root class
  Post-condition must be same or stronger than root class
Prover examines conditions versus source code
"Gold level"

## Slide 31
package Mileage
with Abstract_State => (Trip, -- number of miles so far on this trip (can be reset to 0)
Total) -- total mileage of vehicle since last factory-reset
is
function Trip return Natural; -- Has an implicit Global => Trip
function Total return Natural; -- Has an implicit Global => Total
procedure Zero_Trip
with Global => (Output => Trip), -- In the Global and Depends aspects
Depends => (Trip => null), -- Trip denotes the state abstraction.
Post => Trip = 0; -- In the Post condition Trip denotes
-- the function.
procedure Inc
with Global => (In_Out => (Trip, Total)),
Depends => ((Trip, Total) =>+ null),
Post => Trip = Trip'Old + 1 and Total = Total'Old + 1;
-- Trip and Old in the Post conditions denote functions but these
-- represent the state abstractions in Global and Depends specifications.
end Mileage;

## Slide 32: Ravenscar profile
The full concurrent constructs of Ada are non-deterministic and thus unsuited for formal analysis of real-time properties
The Ravenscar profile is a sub-set of the concurrent constructs:
  Static set of tasks and communication channels
  Single entry per protected object with ceiling locking
  No task rendezvous, requeue or dynamic priorities
  Supported with SPARK 2014
Allows rate monotonic analysis of real-time properties
As side effect, allows very compact run-time environments
AdaCore has run-time certified for DO-178C

## Slide 33: Vermont Technical College
The Vermont CubeSat Laboratory is a SPARK success-story!
  SPARK caught errors as they refactored the software while developing greater understanding of the hardware
  SPARK helped the discipline of the software during turnover as some students graduated and were replaced
  Needed about two weeks to train students in SPARK!
BasicLEO lived for two years and two days, and communicated correctly from launch until re-entry
Now working on AlskanIce CubeSat for buoy data
Prof. Carl Brandon
http://cubesatlab.org/

## Slide 34: C/C++ programming languages
The C programming language is inherently unsafe
  Very low level of abstraction, for instance access to memory
  No strong checking of type
  Very easy, efficient and supported on every target
Standard C++ is perhaps worse by adding complex functionality
  Templates, inheritance, polymorphism, move semantics and operator overloading…
Being a good C/C++ programmer takes a lot of training and skill
MISRA C/C++ tries to counter the weaknesses by adding rules

## Slide 35: MISRA C
A set of software development guidelines for C developed by MISRA (Motor Industry Software Reliability Association)
To be compliant to the MISRA C Guidelines, all mandatory rules shall be met and all required rules and directives shall either be met or subject to a formal deviation
There exists tools to check source code for compliance
Not a free (gratis) standard, but only cost £15 per PDF copy.

## Slide 36: Some rules in MISRA C
Rule 1 (required): All code shall conform to ISO 9899 standard C, with no extensions permitted.
Rule 20 (required): All object and function identifiers shall be declared before use.
Rule 49 (advisory): Tests of a value against zero should be made explicit, unless the operand is effectively Boolean.
Rule 104 (required): Non-constant pointers to functions shall not be used.

## Slide 37: Frama-C
Has similar functionality as SPARK 2014
Use the same theoretical basis for proof engines
Notations provided as comments with special format
  Assertions
  Contracts with pre- and post-conditions
Also allows usage of pointers, not allowed in SPARK 2014
Primary difference between the two is the underlaying language

## Slide 38: Comparison of annonation
/*@
requires \valid(x);
requires *x < 2147483647;
assigns *x;
ensures *x == \old(*x) + 1;
*/
void increment_guarded (int *x)
{
(*x)++;
}
procedure Increment_Guarded
(X : in out Integer)
with
Pre => X < Integer'Last,
Post => X = X'Old + 1
is
begin
X := X + 1;
end Increment_Guarded;

## Slide 39: RTOS for C/C++
C does not specify multitasking, although POSIX is common
Many different RTOS for embedded systems exist for C/C++
  RTEMS, open-source, very popular in space applications
  FreeRTOS, open-source, very popular for embedded systems
  SafeRTOS, variant of FreeRTOS for safety-critical
  VxWorks, proprietary
  QNX, proprietary
  PikeOS, proprietary
A few of these are available in certified versions

## Slide 40: Summary on languages and tools
Ada and C/C++ are commonly used for safety-critical programming
  Only Ada has been designed for safety-critical systems
  C/C++ relies on coding guidelines such as MISRA (or JSF)
Static analysis – sound tool finds all defects, unsound only helps
  Both SPARK and Frama-C are sound tools that provide functional proof
  Find abscense of run-time errors, and prove that code works as specified
Pay attention to a fully certified eco-system with compiler, verification tools and multi-tasking run-time

## Slide 41: References
http://docs.adacore.com/spark2014-docs/html/lrm/index.html
https://www.embedded.com/electronics-blogs/beginner-s-corner/4023981/Introduction-to-MISRA-C
http://www.cubesatlab.org:430/PUBLIC/SPARK-Frama-C-Day-2017.pdf
https://www.adacore.com/uploads/technical-papers/2016-10-SPARK-MisraC-FramaC.pdf
http://www.stroustrup.com/JSF-AV-rules.pdf
Additional reading:
https://www.nasa.gov/sites/default/files/atoms/files/improving_mission_success_of_cubesats_-_tor-2017-01689.pdf

## Slide 43: I3DS project
Space Robotics Cluster (H2020)
  Future robotics platform for ESA
  Led by the PERASPERA project
  6 Operational Grants (OG's)
I3DS – Integrated 3D Sensors
  Thales Alenia Space is coordinator
  SINTEF leads software development, integration and interface definition
TRL 4/5, not certified software

## Slide 45: Project status
Project phases defined as for ESA projects
Kick-off in November 2016, finish November 2018
  SRR in February 2017
  PDR in July 2017
  CDR in February 2018
Now finishing integration phase of project lead by SINTEF
Validation of sensor suite in demonstrators ongoing autumn 2018
Full integration with other OG's in next SRC calls, EROSS project

## Slide 46: Project motivation and goal
Develop and demonstrate a modular sensor suite for space robotics
  Tight cooperation with OG's for middleware, autonomy and sensor fusion
  TASTE framework with AADL and ASN.1 messages for system integration
  Sensors, Instrument Control Unit (ICU) and software at TRL5
Motivation: Reduce development time of space missions
  Abstract away device specific details with standard interface for sensor class
  Allows to use latest sensors available without changing other software
  Reuse sensor interfaces, processing components and ICU hardware
Mission-specific sensor suite with standard components

## Slide 47
Hi-Res Camera
GBit
ToF Camera
GBit
TIR Camera
Gbit
Star Tracker
SpW
Stereo Camera
GBit
Radar
SpW
LIDAR
Gbit & RS232
IMU
RS485
Pattern Projector
Trigger
WA Illumination
Trigger & RS232
Tactile & Torque
LVDS
COTS Hi-Res Camera
GBit

## Slide 48: Demonstrator with orbital use-case
TAS-F in Cannes

## Slide 49: Demonstrator for planetary use-case
ICU
Assy
TAS-I in Torino

## Slide 50: Lab-bench at SINTEF
Integration of sensors with ICU and testing of functionality and real-time properties
Recording of coherent data from all sensors moving on trolley
Sent for mechanical integration at PIAP this week (June 2018)

## Slide 51: Software architecture
Device specific interfaces
Standard sensor class interfaces (ASN.1)
Smart Sensor

## Slide 52: Sensor interfaces
Common ASN.1 commands and queries
  State changes inactive ↔ standby ↔ operational
  Set sample rate and sample batch size of sensor
  Get configuration, state and temperature of sensor
Each sensor class has its own message interface definitions
  Camera, ToF camera, LIDAR, radar, star tracker, IMU, analogue sensors
  Class specific commands, queries and measurements
  Implemented by concrete sensor drivers and emulator
Example: Camera class with shutter time, gain, flash, image frames…

## Slide 53: ASN.1 compiler
Use ASN1CC in project
  Same as used in TASTE framework
  Coded in F# and running on mono
  Outputs code in C and Ada/SPARK
  SPARK allows for formal verification
  Currently use C version due to issues in Ada implementation
uPER encoding for standard messages
Devices interfaces with ACN
https://github.com/ttsiodras/asn1scc
DMU30-Types DEFINITIONS ::= BEGIN
Word-Type[size 16, encoding pos-int]
Real-Type[encoding IEEE754-1985-32]
…
Message-Type[]
{
header NULL [pattern '0101010110101010'B],
message-count[],
axis-x-rate[],
axis-x-acceleration[],
axis-y-rate[],
axis-y-acceleration[],
axis-z-rate[],
axis-z-acceleration[],
aux-input-voltage[],
average-temperature[],
axis-x-delta-theta[],
axis-x-vel[],
axis-y-delta-theta[],
axis-y-vel[],
axis-z-delta-theta[],
axis-z-vel[],
startup-flags[],
operation-flags[],
error-flags[],
checksum NULL [pattern '0000000000000000'B]
}
END

## Slide 54: Computation and throughput load
Lens distortion correction
Histogram equalization
CLAHE
Sensor | Sample size | Rate | Throughput*
HR camera | 2048*2048*2 Bytes = 8 MiB | 10 Hz | 84 Mb/s
Stereo camera | 2*2048*2048*2 Bytes = 16 MiB | 10 Hz | 168 Mb/s
ToF camera | 640*480*5 Bytes = 1500 KiB | 10 Hz | 15 Mb/s
Bilateral filtering
Stereo rectification
Point-cloud generation
*absolute best case

## Slide 55: Instrument Control Unit
ICU build on the Xilinx Zynq UltraScale+ MPSoC
  Mixed-criticality real-time system
  Quad-core ARM Cortex A53 with Xilinx PetaLinux
  Two ARM Cortex R5 real-time processors
  FPGA for bespoke hardware modules
  ARM Mail GPU for processing with support for OpenCV
Runs sensors interfaces and pre-processing algorithms
The Xilinx Zynq UltraScale+ is a complex platform!
Avnet UltraZED-EG SOM

## Slide 58: ICU mixed criticality real-time system
Xilinx PetaLinux on Cortex A53
  Interfaces to GigE vision cameras and COTS sensors
  System interface to OG1/2/3 over GigaBit Ethernet
  Use ZMQ library for high-performance messaging over TCP/IP
  C++ framework developed for sensor interfaces, clients and emulators
  OpenCV used for image processing, e.g. stereo image to point-cloud
Embedded and real-time software on Cortex R5
  ADC polling for tactile and F/T sensors, IMU, triggers, and SpW interfaces…
  Ada/SPARK used for sensor control and processing
Communicate in memory-buffers between cores using OpenAMP

## Slide 59: Cortex A53 with Xilinx PetaLinux

## Slide 60: Cortex R5 #1 with device interfaces

## Slide 61: Cortex R5 #2 with SpaceWire interface

## Slide 62: Ada and SPARK 2014 on the Cortex R5
Use GNAT Pro Developer for ARM with SPARK 2014 tools
  No Ravenscar run-time for the Zynq UltraScale+ MPSoC
  Adapted zero footprint (ZFP) run-time from TMS570 (Cortex R4/5)
  GNAT Pro makes it very easy to reconfigure and recompile run-times
Develop static library with functionality in Ada/SPARK 2014
Xilinx SDK for FreeRTOS, device interfaces, linking and programming
Match ABI and compile flags for GNAT and Xilinx SDK (both use GCC)

## Slide 63: Functionality made in SPARK 2014
Interfaces for IMU and ADC sensors
  Sensor state machines and command handling
  Process, accumulate, and send sensor measurement data
  IMU needs temperature-dependent correction with calibration data
  ADC readings are converted to physical floating-point value
  Hard real-time demands, sampling at 200 Hz and 1000 Hz
Formal proof of correctness for sensor state machine
Flow control and dependencies for data processing
SPARK 2014 allows us to develop code with confidence!

## Slide 64: Forward to a certifiable software system
All critical functionality and Space Wire/Fibre on Cortex R5 and FPGA
Want to have certified Ravenscar run-time on the Cortex R5
  Need to integrate GNAT Pro with Xilinx SDK or the other way around? Reuse drivers?
  Bonus: FPGA gives great opportunities for specialized support hardware (e.g. TMU)
Mixed-criticality with the Cortex A53 and PetaLinux
  Xilinx reVISION provides FPGA-accelerated OpenCV and more
  PetaLinux with accelerated OpenCV for heavy camera pre-processing
  Could use hypervisor such as XtratuM for improved isolation
Coming GNAT for ARM64 allows use on PetaLinux too!

## Slide 65: Conclusions
Future robotics applications require high-performance computer platforms for AI, image processing, machine learning etc.
The Xilinx UltraScale+ MPSoC with accelerated OpenCV and real-time functionality with Ravenscar and SPARK 2014 is very promising!
Need good integration between Xilinx tools generating hardware, PetaLinux, hypervisor, and GNAT Pro for safety-critical real-time code
We want to use this mixed-criticality real-time system and SPARK for our autonomous robots and high-performance edge computing!

## Slide 66
« Smart Sensors for Smart Missions »